## Slide 1: Use of KSKelvin Subckt Symbol from Autogenerated Model
KSKelvin Kelvin Leung
8-3-2024

## Slide 2: Introduction
Purpose
  This guideline show step-by-step instruction to use Subcircuit Symbol from KSKelvin Symbol Library for Autogenerated Model in Qspice
  Focus on subcircuit (.subckt) model of X-device
Device model from Texas Instrument OPA462 is used for this demonstration
  Website : https://www.ti.com/product/OPA462
  Description : OPA462, 180-V, wide bandwidth (6.5 MHz), high-slew rate (25 V/µs) unity-gain stable op amp
  OPA462 Pspice Model (Rev. D) : https://www.ti.com/lit/zip/sbomav9
Prerequisite
  Knowledge of X-device (subcircuit / .subckt) and method of Auto-generate Symbol in Qspice
  Reader can learn importing model and subcircuit from following reference
    Importing 3rd Party Models into Qspice by Mike Engelhardt : https://www.qorvo.com/design-hub/design-tools/interactive/qspice#videos
    General Reference Guideline in KSKelvin’s Github : https://github.com/KSKelvin-Github/Qspice/tree/main/Guideline

## Slide 3: Preparation

## Slide 4: Use KSKelvin Subckt Symbol from Autogenerated Model
Step 1 : Model Study
  In general, model is named as .lib, .txt, .mod or .sub etc…
  Use text editor to open and inspect the model
    Only unencrypted model can be used for auto generate symbol in Qspice
    [1] Identify the .subckt of device (in this example, OPA462), and confirm its pin sequence
    [2] Verify if this subcircuit has dependent .subckt. If X-device can be found between .subckt and .ends, this device will call other subcircuit
[1]
[2]
other subcircuit